## Slide 1: Physical Attacks against Neural Networks Benefits from an adversary’s viewpoint Benoit COQUERET, Gabriel ZAID

## Slide 2: Context
* https://artificialintelligenceact.eu/the-act/
AI Act*, kesako ?
Creation of regulations ranging from CE marking to a marketing ban on AI systems and models placed on the market.
AI Act, who is affected?
All suppliers, developers and distributors of AI systems whose head office is in the EU or who market solutions in the EU.
AI Act, which systems are affected?
AI at unacceptable risk
High-risk AI
Low-risk AI
Minimal-risk AI
Ensure robustness, accuracy and resilience to cyber-attacks

## Slide 3: Physical Attacks against Neural Networks (in this talk)
Fidelity-based extraction attack
Evasion attacks
‘‘When Side-Channel Attacks Break the Black-Box Property of Embedded Artificial Intelligence.’’, Coqueret et al., AISec ‘23

## Slide 4: Evasion attack
Could be difficult to consider in practice
  White-box scenario: knowledge of the IA architecture, weights, activation functions, etc…
  Black-box scenario: partial knowledge on the AI system (e.g., logits)
Practical issue: How can we generate adversarial examples without any knowledge on the device?
It’s a 7 !
It’s a 3 !
Adversarial examples, KESAKO ?

## Slide 5: Evasion attack
It’s a 3 !
Practical issue: How can we generate adversarial examples without any knowledge on the device?
Our idea :
  1) Extraction of the logits through the use of side-channel attacks
  2) Use the state-of-the art adversarial attacks (e.g. ZOO*)
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
It’s a 7 !

## Slide 6: Evasion attack
  Device: ARM Cortex-M7 MCU on a STM32F767 board (216 MHz)
  Embedded AI: a 8-bit quantized denseNET (weights, activations, inputs) with NNOM* tool
  Classification problem: 10 classes (MNIST)
  Channel: Electromagnetic signal (EMV-Technik RF-U 2,5 probe)
* GitHub - majianjia/nnom: A higher-level Neural Network library for microcontrollers.

## Slide 7: Evasion attack
It’s a 0
It’s a 1
It’s a 2
It’s a 3
It’s a 4
It’s a 5
It’s a 6
It’s a 7
It’s a 8
It’s a 9
Softmax
Neural network
Probability
Logits

## Slide 8: Evasion attack
  Targeted function: Softmax function
C code related to the softmax function
vec_in

## Slide 9: Evasion attack
  Side-Channel attacks

## Slide 10: Evasion attack
  Experimental results
  Template
  Logistic regression
Deep learning
Logits
We successfully extract all the logits within 5 traces
K-means

## Slide 11: Evasion attack
  Practical issue: How can we generate adversarial examples without any knowledge on the device?
  Our idea :
  1) Extraction of the logits through the use of side-channel attacks
  2) Use the state-of-the art adversarial attacks (e.g. ZOO*)
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
It’s a 7 !
x3
Logits

## Slide 12: Evasion attack
  Generate an adversarial example
    Application of the Zeroth Order Optimization* (ZOO) method
  Recap (ZOO)
  Let be an image and a wrong targeted class that an attacker wants to predict , she looks for an adversarial example such that the following relation is satisfied:
  with
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
Original image
Adversarial example

## Slide 13: Evasion attack
  Practical issue: How can we generate adversarial examples without any knowledge on the device?
  Our idea :
  1) Extraction of the logits through the use of side-channel attacks
  2) Use the state-of-the art adversarial attacks (e.g. ZOO*)
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
It’s a 3 !

## Slide 14: Physical Attacks against Neural Networks (in this talk)
Fidelity-based extraction attack
Evasion attacks
‘‘When Side-Channel Attacks Break the Black-Box Property of Embedded Artificial Intelligence.’’, Coqueret et al., AISec ‘23

## Slide 15: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
    Better than accuracy-based extraction attack if we want to transfer attack (e.g. adversarial examples)
  ‘‘High accuracy and high fidelity extraction of neural networks’’, Jagielski et al. Usenix Security 20
  ‘‘Reverse-engineering deep ReLU networks’’, Rolnick et al. ICML 2020
  ‘‘Cryptanalytic extraction of neural network models’’, Carlini et al. Crypto 2020
Hypotheses (ReLU activation function + knowledge of the architecture)
with a linear combination of et

## Slide 16: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
  ‘‘High accuracy and high fidelity extraction of neural networks’’, Jagielski et al. Usenix Security 20
  ‘‘Reverse-engineering deep ReLU networks’’, Rolnick et al. ICML 2020
  ‘‘Cryptanalytic extraction of neural network models’’, Carlini et al. Crypto 2020
Neurons are activated/deactivated depending on and  8 possible linear combinations

## Slide 17: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
  ‘‘High accuracy and high fidelity extraction of neural networks’’, Jagielski et al. Usenix Security 20
  ‘‘Reverse-engineering deep ReLU networks’’, Rolnick et al. ICML 2020
  ‘‘Cryptanalytic extraction of neural network models’’, Carlini et al. Crypto 2020
Neurons are activated/deactivated depending on and  8 possible linear combinations

## Slide 18: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
  ‘‘High accuracy and high fidelity extraction of neural networks’’, Jagielski et al. Usenix Security 20
  ‘‘Reverse-engineering deep ReLU networks’’, Rolnick et al. ICML 2020
  ‘‘Cryptanalytic extraction of neural network models’’, Carlini et al. Crypto 2020

## Slide 19: Using side-channel attacks to extract the critical points (Attack overview)

## Slide 20: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
Algorithm
  1) Draw 2 points and capture the physical signal and
  2) From and , use SCA to identify if are in the same state
  3) If , goto (1), else draw a point and capture the physical signal
  4) From , and , use SCA to identify if or are in the same state
  5) For that are not in the same state, draw a point
  6) …

## Slide 21: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
Compute least-squares solution to equation

## Slide 22: Using side-channel attacks to extract the critical points (SCA Vulnerability)

## Slide 23: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
Algorithm
  1) Draw 2 points and capture the physical signal and
0x00000000
0xFFFFFFFF
If
If

## Slide 24: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
Algorithm
  1) Draw 2 points and capture the physical signal and
  2) From and , use SCA to identify if are in the same state
K-means

## Slide 25: Fidelity-based extraction attack
Example “model extraction attack”
  Goal: Stealing IP of a model AND the performance of a model
Algorithm
  1) Draw 2 points and capture the physical signal and
  2) From and , use SCA to identify if are in the same state
  3) If , goto (1), else draw a point and capture the physical signal
  4) From , and , use SCA to identify if or are in the same state
  5) For that are not in the same state, draw a point
  6) …
Final Step: Compute least-squares solution to equation

## Slide 26: Fidelity-based extraction attack
  Device: ARM Cortex-M7 MCU on a STM32F767 board (216 MHz)
  Embedded AI: a 32-bit neural networks implemented with X-Cube-AI* tool
  Problem: Regression and Classification tasks
  Channel: Electromagnetic signal (EMV-Technik RF-U 2,5 probe)
* X-CUBE-AI - AI expansion pack for STM32CubeMX - STMicroelectronics
Type of architectures | Nb of parameters | Nb of targets
Small MLP | < 200,000 | 7
MLP | 935,370 | 1
Large MLP | 1,721,802 | 1
MobileNetv1-short | 5,234 | 1

## Slide 27: Fidelity-based extraction attack (for classification task)
  How assessing the efficiency of fidelity-based extraction attacks (for classification task)?
  1) Number of queries required to extract all the neurons
  2) Fidelity metric = s.t. (resp. ) is the targeted model (resp. the copy)
  3) Weight difference =
  ‘‘Cryptanalytic extraction of neural network models’’, Carlini et al. Crypto 2020
Architecture (Classification) | Nb of parameters | Nb of queries | Fidelity
3072-256-256-256-64-10 | 935,370 |  | 
3072-512-256-64-10 | 1,721,802 |  | 
TruncatedMobileNetv1 (CNN) | 5,234 |  | 
Architecture (Classification) | Nb of parameters | Nb of queries | Fidelity
3072-256-256-256-64-10 | 935,370 |  | 
3072-512-256-64-10 | 1,721,802 |  | 
TruncatedMobileNetv1 (CNN) | 5,234 |  | 
  New targeted architectures
First extraction of CNN using cryptanalytical-based extraction attacks by taking benefits of SCA !

## Slide 28: Physical Attacks against Neural Networks (in this talk)
Fidelity-based extraction attack
Evasion attacks
‘‘When Side-Channel Attacks Break the Black-Box Property of Embedded Artificial Intelligence.’’, Coqueret et al., AISec ‘23

## Slide 29: Conclusion
Combining Software & Hardware attacks is beneficial to reduce adversary’s knowledge.
Side-channel attacks can be used to prevent some issues with software attacks.
  Performing fidelity-based extraction attacks on CNN architectures.
  Mitigating the effect of special case neurons.
Extends the security threats against embedded AI system.
Needs of finding adequate countermeasures which not alter the performance of embedded AI too much.
Benoit will present his work during the SemSecuElec Seminar this Friday 
  https://www.creachlabs.fr/en/seminars-keeping-date-latest-research/semsecuelec-seminar/cryptanalytical-extraction-complex-neural-networks-black-box-settings

## Slide 30: Merci Contact: gabriel.zaid@thalesgroup.com

## Slide 31: Fidelity-based vs. Accuracy-based extraction attack
Accuracy-based extraction: stealing the performance task ONLY
Fidelity-based extraction: stealing the performance task AND the IP of the model
Man
Man
Man
Accuracy-based extraction
Fidelity-based extraction
Woman
Attack
Woman
Attack
Woman
The fidelity-based extraction is beneficial to mount higher-level attacks against it, e.g., generation of adversarial examples in a white-box scenario

## Slide 32: Fidelity-based extraction attack
Average Success Rate of retrieving each neuron state in 1 trace (using K-means): 86,3%
  Example of SNR obtained on a MLP with 15 neurons
Time samples

## Slide 33: Fidelity-based extraction attack (for regression task)
  How assessing the efficiency of fidelity-based extraction attacks (for regression task)?
  1) Number of queries required to extract all the neurons
  2) Weight difference =
Architecture (Regression) | Nb of parameters | Nb of queries | Weight diff.
784-128-1 | 100,480 | Carlini et al. | Carlini et al.
10-20-20-1 | 620 | Carlini et al. | Carlini et al.
40-20-10-10-1 | 1,110 | Carlini et al. | Carlini et al.
Architecture (Regression) | Nb of parameters | Nb of queries | Weight diff.
784-128-1 | 100,480 |  | 
10-20-20-1 | 620 |  | 
40-20-10-10-1 | 1,110 |  | 
  ‘‘Cryptanalytic extraction of neural network models’’, Carlini et al. Crypto 2020
/2
x4
x2
x2,700
x700
x32,000
  Comparison with SOTA